## Slide 1: Using a joystick to control two motors -Digital electronics 2 project
Created and presented by:
Nolwenn Violette and Frederick Jennings

## Slide 2: Task and preparation
Our task was to control several SG90 servo motors using HW-504 analog joysticks.
Started by finding the datasheets for both components.
We developed two simple test code for testing
We agreed on certain specifications:
  That we’d use one joystick for two motors
  Each motor would be for one axis
  If we had time we wanted different modes

## Slide 3: Joystick
The joystick sends two analog signals
The ADC can only use 1 channel at once
Had to use a finite state machine to change signals.

## Slide 4: Servo motors
The motors use PWM signal.
Two motors requires a PWM each.
The length of the duty cycle dictates the angle to which it turns.
One timer used to generate both signals.

## Slide 8: Additional features
We add debouncing as the mode switching wasn’t working properly.

## Slide 9: Video demonstration